## Slide 1: SoftRing: Taming the Reactive Model for Software Defined Networks
Chengchen Hu, Kaiyu Hou, Hao Li, Ruilong Wang
Peng Zheng, Peng Zhang, Huanzhao Wang
MOE KLINNS Lab
Xi’an Jiaotong University

## Slide 2: Match-Action Abstraction
Software Defined Networking (SDN) employs a Match-Action model as processing abstraction
A packet: ① match a rule in switches
  ② execute the related actions
          Forward, Drop, Modify
Flow entry stored in Flow Table

## Slide 3: Proactive vs. Reactive
Proactive
Pre-install flow entry in switches
Anticipate the network issues in advance
Reactive
Switches invoke the controller on network event
Controller pushes corresponding flow entry
Notes: To push the flow rules

## Slide 4: Proactive Model Only?
Limited flow entry memory in switch
  TCAM, up to 5000~ flow entries
  Limited flexibility, finer-grained control
Unawareness of data plane
  Controller cannot be aware of failures
  Flow entry removed: bugs, attacks
    Continuously drop packets
Notes: Therefore, we believe the Proactive model should work together with reactive model

## Slide 5: Overhead in Reactive
Reactive introduces communicate overhead between controller and switches (South-Bound Interface)
Table-miss event
  One common trigger of reactive
  Example: OpenFlow
Controller
Switch
Notes: Generally, we believe the reactive model should coexist with proactive model as a complement,

## Slide 6: Table-miss
New incoming packet doesn’t match any flow entry
  Raise a Table-miss event
Controller
Switch
Packet
Notes: Generally, we believe the reactive model should coexist with proactive model as a complement,

## Slide 7: Table-miss
Switch buffers the packet
Sends a Packet-in message to controller
  first 128 bytes of the packet
Packet
Buffer Packet in Switch
Packet-in
128 Byte
Controller
Switch
Packet-out
Buffer Id

## Slide 8: Table-miss
The buffer overflows
Switch has to send the entire packet through the Packet-in message
Packet
Packet-in
1500 Byte
Packet
Packe
Controller
Switch
Packet
Packet
Packet
Packet-out
1500 Byte
SBI bandwidth overhead increases
Latency to install the new entry increases
(5ms to 100ms)
Notes: If too many new flow arrived on a short period of time,
Which finally affect the performance of whole network systems.

## Slide 9: When Does Reactive Happen?
Small flows come successively.
  20% traffic occupies 80% of total flows.
Limited flow entry memory, replacement
  E.g., LRU Policy
  Subsequent packets of TCP can trigger Table-miss
Subsequent packets also trigger Table-miss
  Before related new rule installed
1
2
3
Notes: Generally, we believe the reactive model should coexist with proactive model as a complement,

## Slide 10: Where to buffer the Table-miss packet?
Keep in Switch
  Buffer overflow: new flow exceeds 0.26% of switch capacity
Send to Controller
  Only 0.06% of the traffic consume all the control bandwidth
Brand | Model | Port | Buffer | Control BW
Pica8 | AS7712-32X | 100GbE*32 | 16MB | 1000Mbps
Brocade | ICX7750-26Q | 40GbE*26 | 12.2MB | 1000Mbps
Dell | Z9100-ON | 100GbE*32 | 16MB | 1000Mbps
Huawei | CE8860 | 100GbE*32 | 16MB | N/A
Netgear | M5300-52G | 48+10GbE*4 | 4MB | 10Gbps
Notes: Generally, we believe the reactive model should coexist with proactive model as a complement,

## Slide 11: Goal of SoftRing
Reduce Buffer Reduce Bandwidth
Less Packet Drop Compatibility
1
2
3
4
Notes: Generally, we believe the reactive model should coexist with proactive model as a complement,

## Slide 12: Popular Restaurant Policy
Popular restaurant cannot have enough tables to serve everyone (“table-miss”)
Waiters: record the customer，arrange a waiting number
Customers: walk away and back later when the seat availability.

## Slide 13: Basic Idea
Extend loops in network
Remaining bandwidth and memory in dataplane
  Internet: > 50%
  Data Center: > 75%
Accurate control of packet forwarding

## Slide 14: Three Challenges
Seek and Select waiting-loops
Enforce waiting-loop policy in switches
Dynamically adjust waiting-loops
1
2
3
Notes: Generally, we believe the reactive model should coexist with proactive model as a complement,

## Slide 15: Seek and Select
Loop Seeking Algorithm
(collect enough loops as waiting-loop candidate)
Loop Selection Algorithm
(select a loop subset to cover all the switches)
1

## Slide 16: Loop Seeking Algorithm
Based on Johnson’s loop searching algorithm
  Directed graph
Accelerate
  Graph partition
  Loop length and scale control
  Random shuffle
Virtual Loop
  𝑣1→𝑣2→…→𝑣2→𝑣1
Waiting-loop
Candidate Set
Notes: Graph partition: calculation simultaneously
Random shuffle: increase loop diversity

## Slide 17: Loop Selection Algorithm
Select a loop subset to meet the requirements:
  Cover all the switches
  Minimize the extra delay
  Bandwidth in Data Plane
  Minimize the extra flow entries
Map to weighted set cover problem
Notes: Graph partition: calculation simultaneously
Random shuffle: increase loop diversity

## Slide 18: Switch Enforcement
2
 | Priority | Match | Action | Timeout
OpenFlow | 0 | * | ① Buffer Table-miss packet in switch ② Send Packet-in with 128 Bytes | 0
ES (Entry Switch) | 0 | * | ① Send Packet-in with 128 Bytes ② Push VLAN = 1 ③ Set TTL = β ④ Send to next switch by queue | 0
LS (Loop Switch) | 1 | VLAN = 1 in-port = pre-switch | ① Set TTL = TTL -1 ② Send to next Switch by queue | 0

## Slide 19: Switch Enforcement
VLAN tag: distinguish waiting-loop packet
2
 | Priority | Match | Action | Timeout
OpenFlow | 0 | * | ① Buffer Table-miss packet in switch ② Send Packet-in with 128 Bytes | 0
ES (Entry Switch) | 0 | * | ① Send Packet-in with 128 Bytes ② Push VLAN = 1 ③ Set TTL = β ④ Send to next switch by queue | 0
LS (Loop Switch) | 1 | VLAN = 1 in-port = pre-switch | ① Set TTL = TTL -1 ② Send to next Switch by queue | 0

## Slide 20: Switch Enforcement
VLAN tag: distinguish waiting-loop packet
Priority: never affect normal traffic
2
 | Priority | Match | Action | Timeout
OpenFlow | 0 | * | ① Buffer Table-miss packet in switch ② Send Packet-in with 128 Bytes | 0
ES (Entry Switch) | 0 | * | ① Send Packet-in with 128 Bytes ② Push VLAN = 1 ③ Set TTL = β ④ Send to next switch by queue | 0
LS (Loop Switch) | 1 | VLAN = 1 in-port = pre-switch | ① Set TTL = TTL -1 ② Send to next Switch by queue | 0

## Slide 21: Switch Enforcement
VLAN tag: distinguish waiting-loop packet
Priority: never affect normal traffic
TTL: avoid endless loop
2
 | Priority | Match | Action | Timeout
OpenFlow | 0 | * | ① Buffer Table-miss packet in switch ② Send Packet-in with 128 Bytes | 0
ES (Entry Switch) | 0 | * | ① Send Packet-in with 128 Bytes ② Push VLAN = 1 ③ Set TTL = β ④ Send to next switch by queue | 0
LS (Loop Switch) | 1 | VLAN = 1 in-port = pre-switch | ① Set TTL = TTL -1 ② Send to next Switch by queue | 0

## Slide 22: Switch Enforcement
2
Type | Priority | Match/Data Field | Action | Timeout
Packet-out | / | Buffer ID or Entire Packet | Forwarding | /
Flow-add | >2 | ip_src ip_dst etc. | Forwarding | normal
Controller-to-Switch Message: OpenFlow
Type | Priority | Match/Data Field | Action | Timeout
Flow-add | >2 | VLAN = None ip_src ip_dst etc. | Forwarding | normal
Flow-add | >2 | VLAN = 1 ip_src ip_dst etc. | ① Pop VLAN ② Reset TTL ③ Forwarding | short
Controller-to-Switch Message: SoftRing

## Slide 23: Handling the Dynamic
3
Forbidden Link: overloaded or failed links
Re-execute: Only Loop Selection Algorithm (< 1s)

## Slide 24: Handling the Dynamic
3

## Slide 25: SoftRing: Implementation

## Slide 26: SoftRing: Implementation
Controller:
  Floodlight
Switch:
  Open vSwitch: Software Switch
  ONetSwitch 30: Hardware Switch
  Fattree(4) with 20 ONetSwitch

## Slide 27: SoftRing: Implementation
Loop ID | Switch ID |  |  |  |  |  |  |  | Loop Length
1 | 1 | 10 | 20 | 14 | 6 | 13 | 17 | 9 | 8
2 | 2 | 9 | 17 | 13 | 5 | 14 | 19 | 10 | 8
3 | 3 | 12 | 19 | 16 | 8 | 15 | 18 | 11 | 8
4 | 4 | 11 | 18 | 15 | 7 | 16 | 20 | 12 | 8

## Slide 28: Evaluation

## Slide 29: Evaluation
100% Coverage,
  Virtual Loop used in last three topology

## Slide 30: Evaluation

## Slide 31: Benefit of SoftRing

## Slide 32: Cost of SoftRing
Average Packet Delay in Different Reactive Packet Rate
0.2%
2.9%

## Slide 33: Cost of SoftRing
Static Flow Entries Used in One Switch

## Slide 34: Conclusion
SoftRing
A reactive packet goes through a pre-computed waiting-loop before get related rules from controller.
Claim
We advocate the coexistence of proactive model and reactive model.
Evaluation
Reduce the control channel bandwidth up to 80%.
With the cost of 3 flow entries, minor latency.

## Slide 35: Questions ?
Thank You